## Slide 1
Camera Show
Operating Modes & Detection Principles
Technical Overview | 5 Detection Modes | Engineering Reference
Normal
Read 2D
Compare Image
Check LED
Blink LED
camera_show application | Engineering Reference

## Slide 2
System Overview
> Windows Forms C# application (.NET 4.8)
> Emgu CV - OpenCV wrapper for image processing
> ZXing - Barcode / QR code decoding library
> DirectShow VideoCapture - live camera at ~10 fps
> ROI-based processing - user-drawn rectangle per step
> CSV config files - per-step camera & mode parameters
> Result: test_head_{head}_result.txt -> PASS / FAIL
Mode Summary
Mode | Purpose | Output
Normal | Live camera view | Display only
Read2D | Barcode / QR decode | Decoded text + PASS/FAIL
Compare Image | Template matching | PASS / FAIL
Check LED | Sustained color detect | PASS / FAIL
Blink LED | Frequency measurement | Freq (Hz) + PASS/FAIL

## Slide 3
Mode 1: Normal — Live View
MODE 1 / 5
DISPLAY ONLY
No detection No analysis No result output
Detection Principle
1
Acquire frame from camera (VideoCapture)
2
Render frame to PictureBox UI control
3
Check for black frames: mean BGR < 8.0
4
5 consecutive black frames -> reopen camera
5
Sleep 100 ms -> repeat at ~10 fps
Use case: Operator visual inspection during setup | Camera health monitoring

## Slide 4
Mode 2: Read2D — Barcode / QR Code Reading
MODE 2 / 5
Purpose: Detect and decode 1D/2D barcodes within a defined ROI using Canny edges + ZXing with rotation-invariant sweep.
1. Acquisition
Acquire Frame
->
Rotate by AdjustDegree
->
Crop to ROI
2. Edge Detection
Grayscale + Threshold
->
Canny Edges
->
Find Contours
3. Decode
ZXing Pass 1 (full ROI)
->
ZXing Pass 2 (rect+rotate)
->
Stop on success
4. Validation
Check length == DigitSn
->
PASS -> write file
->
FAIL -> AutoScale
Timeout (default 10,000 ms): elapsed >= timeout -> write FAIL and exit. AutoScale shifts ROI in expanding spiral (+-1, +-2, +-3 px) on repeated failures.

## Slide 5
Mode 2: Read2D — Algorithm Details
Rectangle Detection (Canny)
o Grayscale -> Binary threshold @ 150
o Canny edges: high=180, low=120
o FindContours (RetrType.List)
o ApproxPolyDP epsilon = arc_length x 0.1
o Keep: area > 50 px AND exactly 4 vertices
o Validate: all 4 exterior angles = 70-100 deg
ZXing Decode Strategy
Pass 1 - Full ROI direct decode
ZXing attempts decode on full cropped image
If success -> validate length -> done
Pass 2 - Rotation sweep per rectangle
For each detected rectangle:
Rotate: 0, 5, 10, ..., 85 degrees
ZXing decode at each angle
Stop on first successful decode
Validation - DigitSn check
Decoded length must equal DigitSn (default 13)
On FAIL: AutoScale spiral ROI shift

## Slide 6
Mode 3: Compare Image — Template Matching
MODE 3 / 5
Purpose: Verify that a reference image is visually present in the live frame using KAZE feature matching and homography.
1 Acquire frame -> Crop to ROI
2 Load reference image from disk (Image1.png, Image2.png ...)
3 KAZE feature detection & description on both images
4 Flann KNN matching (k=2) + Lowe's ratio test (0.80)
5 VoteForSizeAndOrientation (max deviation 20 deg)
6 Compute homography -> objectFound = true
7 Advance NumberCompare -> load next image ROI
8 No more ref images -> write PASS and exit
Sequence Logic
Each step can have multiple
reference images.
NumberCompare counter tracks
the current image index.
Image1.png -> check -> advance
Image2.png -> check -> advance
Image3.png not found -> PASS
(no more images = all matched)
Each image has its own ROI
coordinate file.
On object NOT found:
ReAdjust restores camera
baseline settings.

## Slide 7
Mode 3: Compare Image — KAZE & Homography Details
KAZE Feature Matching
KAZE Detector
Scale-space detector, robust for textured objects
Detects keypoints in model AND observed image
Computes binary descriptors for each keypoint
Flann-based Matcher
LinearIndexParams + SearchParams
KNN matching: k = 2 nearest neighbors
Lowe's Ratio Test (threshold = 0.80)
Keep match if:
best_dist < 0.80 x second_best_dist
Discards ambiguous / weak matches
VoteForSizeAndOrientation
Discard if scale/rotation deviation > 20 deg
Homography Validation
Minimum 4 unique matches required
GetHomographyMatrixFromMatchedFeatures
Reprojection threshold: 2 pixels
Valid homography -> objectFound = true
Parameter | Value
Lowe ratio test | 0.80
Min matches (homography) | 4
Reprojection threshold | 2 px
Max orientation deviation | 20 deg

## Slide 8
Mode 4: Check LED — Sustained Color Detection
MODE 4 / 5
Purpose: Verify that a target LED color is present in the ROI for a minimum continuous duration.
Detection Principle
Acquire frame -> Convert to BGR & HSV -> Crop to ROI
Apply color range mask (user-configurable):
BGR mode: image.InRange(BgrLow, BgrHigh)
HSV mode: image.InRange(HsvLow, HsvHigh)
Count non-zero pixels in mask -> redpixels
If redpixels >= HsvMask -> check elapsed timer
If timer >= HsvTimeout -> PASS (color sustained)
Else -> reset timer (color must be continuous)
Advance NumberCheckLed -> load next LED step ROI
Key Parameters
Parameter | Default | Description
HsvMask | 10 px | Min pixels for 'color on'
HsvTimeout | 100 ms | Min continuous duration
Color space | Config | BGR or HSV (user set)
Persistence Logic
Color detected continuously:
Timer counts up -> >= HsvTimeout -> PASS
Color drops -> Timer RESETS -> must restart

## Slide 9
Mode 5: Blink LED — Frequency & Duty Cycle Measurement
MODE 5 / 5
State Machine (per frame)
Apply color mask (same as Check LED)
mask = (redpixels >= HsvMask)
On color ON (mask=true):
TimeHigh = StopWatchHigh.Elapsed
StopWatchLow.Restart()
On color OFF (mask=false):
TimeLow = StopWatchLow.Elapsed
StopWatchHigh.Restart()
TricCal = true (flag next calc)
On transition OFF->ON (TricCal):
Period = TimeLow + TimeHigh (ms)
FreqSup += 1 / (Period / 1000)
DutySup += TimeHigh / Period x 100
Counter++
Formulas & Measurement Window
Frequency: f = 1 / ((TimeLow + TimeHigh) / 1000) [Hz]
Duty Cycle: D = TimeHigh / (TimeLow + TimeHigh) x 100 [%]
Measurement Window
Min 2000 ms accumulated (TimeAckMin)
countSup = 2000 / (TimeLow + TimeHigh)
CounterMax = Map(countSup, 0-2000, 1-1200)
Accumulate FreqSup and DutySup over CounterMax samples
Final Result
Frequency = FreqSup / Counter
Duty = DutySup / Counter
-> pass to 3-sample stability validation

## Slide 10
Mode 5: Blink LED — Stability Validation & Thresholds
MODE 5 / 5
3-Sample Rolling Stability Check
Maintain rolling buffer of last 3 frequency measurements
Compute average of the 3 samples
For each sample: |avg - sample| / avg x 100 = % deviation
If ALL 3 samples <= 5.0% -> FlagResult = true -> PASS
If ANY sample > 5.0% -> FlagResult = false -> measure again
Write frequency (4 decimal places Hz) + PASS to result file
Example: samples = [49.98, 50.01, 50.02] avg = 50.003 deviations: 0.046%, 0.014%, 0.034% -> all < 5% -> FlagResult = true -> PASS
Key Thresholds
Parameter | Value | Description
TimeAckMin | 2000 ms | Min measurement window
MaxDiffPercent | 5.0 % | Max deviation (3 samples)
HsvMask | 10 px | Min pixels for color on
CounterMax | 1-1200 | Dynamically scaled
Output
Frequency: 4 decimal places (Hz)
Duty Cycle: 4 decimal places (%)
Pixel count shown on overlay
File format:
{frequency_value}\r\nPASS

## Slide 11
Detection Principles — Mode Comparison Summary
Mode | Core Algorithm | Key Inputs | Key Thresholds | Output
Normal | Frame display only | Live video | None | Visual only
Read2D | Canny edges + ZXing + rotation sweep | ROI, DigitSn, AdjustDegree | Canny 180/120 Angle 70-100 deg Area > 50 px | Decoded text PASS/FAIL
Compare Image | KAZE + Flann KNN + Homography | ROI, Ref images | Lowe 0.80 Min 4 matches Reproj 2 px | Object found (binary)
Check LED | Color mask BGR/HSV + persistence timer | ROI, color range HsvMask, HsvTimeout | >= 10 px >= 100 ms sustained | Color detected (binary)
Blink LED | State machine + freq averaging + stability check | ROI, color range HsvMask | +-5% stability 2000 ms window 3-sample rolling | Freq (Hz) Duty (%) PASS/FAIL

## Slide 12
Shared Infrastructure Across All Modes
ROI — Region of Interest
* User draws rectangle via mouse drag on live frame
* Coordinates saved per step to Rectangle*.txt files
* AutoScale: spiral shift +-1-3 px on repeated decode failure (Read2D)
Camera Configuration
* Settings stored in CSV files - one per test step / mode
* Configurable: zoom, pan, tilt, contrast, brightness,
* saturation, sharpness, gain, focus, exposure
* Skip list: opt-out per property for problematic cameras
Result Output
* File: test_head_{head}_result.txt
* Format: {result_value}\r\n{PASS|FAIL}
* Timeout (default 10,000 ms) -> writes FAIL on expiry
* Retry: EditValueCamDiv3 allows up to 3 retries before FAIL
Failure Recovery
* ReAdjust.Run() - restores baseline camera settings on failure
* EditValueCamDiv3.Process() - tracks retry count
* Black frame detection - reopens camera on hardware issue
* 3-second reopen cooldown - prevents hardware damage